## Slide 1: Describing Inter-VLAN Routing

## Slide 2
Layer 3 switches usually have packet-switching throughputs in the millions of packets per second (pps).
All Catalyst multilayer switches support the following types of Layer 3 interfaces:
  Routed port
  Switch virtual interface (SVI)
High-performance switches, such as the Catalyst 6500 and Catalyst 4500, are able to perform most of the router’s functions.
Several models of Catalyst switches require enhanced software for specific routing protocol features.
Layer 3 Switching Operation and Configuration Introduction to Layer 3 Switching
Notes: 5.3.1.1 Introduction to Layer 3 Switching

## Slide 3: Introduction to Inter-VLAN Routing
Because VLANs isolate traffic to a defined broadcast domain and subnet, network devices in different VLANs cannot communicate with each other natively.
The devices in each VLAN can communicate to the network devices in another VLAN only through a Layer 3 routing device
The following devices can provide inter-VLAN routing:
  Any Layer 3 multilayer Catalyst switch
  Any external router with an interface that supports trunking (router-on-a-stick)
  Any external router or group of routers with a separate interface in each VLAN

## Slide 4
The Cisco Switch Database Manager (SDM) provides multiple templates for the Cisco Catalyst 2960 switch.
The SDM lanbase-routing template can be enabled to allow the switch to route between VLANs and to support static routing.
Use the show sdm prefer command to verify which template is in use.
The SDM template can be changed in global configuration mode with the sdm prefer command.
Layer 3 Switching Operation and Configuration Configuring Static Routes on a Catalyst 2960
Notes: 5.3.1.5 Configuring Static Routes on a Catalyst 2960

## Slide 5: Introduction to Inter-VLAN Routing

## Slide 6: Inter-VLAN Routing Using an External Router
Configure subinterfaces so that R1 will route between PC1 (VLAN10) and PC2 (VLAN20).
Configure a trunk so that R1 will receive the traffic that needs to be routed.

## Slide 7: Routing with an External Router Configuration
Configure router subinterface for routing of VLAN 10 / VLAN 20 traffic.
R1(config)# interface ethernet 0/0.10
R1(config-subif)# encapsulation dot1q 10
R1(config-subif)# ip address 10.0.10.1 255.255.255.0
R1(config)# interface ethernet 0/0.20
R1(config-subif)# encapsulation dot1q 20
R1(config-subif)# ip address 10.0.20.1 255.255.255.0
Configure a subinterface for native VLAN traffic.
R1(config)# interface ethernet 0/0.1
R1(config-subif)# encapsulation dot1q 1 native
R1(config-subif)# ip address 10.0.1.1 255.255.255.0

## Slide 8: Verify configuration

## Slide 9: Routing with an External Router Configuration
Configure switch trunk port. Allow only VLAN 1, 10, and 20 traffic.
SW1(config)# interface ethernet 0/0
SW1(config-if)# switchport trunk encapsulation dot1q
SW1(config-if)# switchport mode trunk
SW1(config-if)# switchport trunk allowed vlan 1,10,20

## Slide 10: External Routers: Advantages Disadvantages
The following are advantages of external router usage:
An external router works with any switch because Layer 3 services are not required on the switch. Many switches do not contain Layer 3 forwarding capability, especially switches that are used at the access layer of a hierarchical network.
The implementation is simple. Only one switch port and one router interface require configuration.
If the network design includes only Layer 2 switches, the design and also the process for troubleshooting traffic flow become very simple because there is only one place in the network where VLANs interconnect.

## Slide 11: External Routers: Advantages Disadvantages
The following are disadvantages of external router usage:
The router is a single point of failure.
A single traffic path may become congested. With a router-on-a-stick model, the trunk link is limited by the speed of the router interface being shared across all trunked VLANs
Latency may be introduced as frames leave and reenter the switch chassis multiple times and as the router makes software-based routing decisions.

## Slide 12
Today’s routing has become faster and cheaper and can be performed at hardware speed.
Routing can be transferred to core and distribution devices with little to no impact on network performance.
Many users are in separate VLANs, and each VLAN is usually a separate subnet. This implies that each distribution switch must have IP addresses matching each access switch VLAN.
Layer 3 (routed) ports are normally implemented between the distribution and the core layer. This model is less dependent on spanning tree, because there are no loops in the Layer 2 portion of the topology.
Layer 3 Switching Operation and Configuration Inter-VLAN Routing with Switch Virtual Interfaces
Notes: 5.3.1.2 Inter-VLAN Routing with Switch Virtual Interfaces

## Slide 13: Inter-VLAN Routing Using Switch Virtual Interfaces
An SVI is a virtual interface configured within a multilayer switch, as compared to external router configuration
An SVI can be created for any VLAN that exists on the switch. Only one VLAN associates with one SVI.

## Slide 14: Switch Virtual Interfaces
An SVI is “virtual” in that there is no physical port dedicated to the interface, yet it can perform the same functions for the VLAN as a router interface would
Can be configured in much the same way as a router interface (IP address, inbound/outbound access control lists [ACLs], and so on).
The SVI for the VLAN provides Layer 3 processing for packets to or from all switch ports associated with that VLAN.
By default, an SVI is created for the default VLAN (VLAN1) to permit remote switch administration.
Additional SVIs must be explicitly created and the number used corresponds to the VLAN tag associated.

## Slide 15
SVIs are created the first time the VLAN interface configuration mode is entered for a particular VLAN SVI.
Enter the interface vlan 10 command to create an SVI named VLAN 10.
The VLAN number used corresponds to the VLAN tag associated with data frames on an 802.1Q encapsulated trunk.
When the SVI is created, ensure that the specific VLAN is present in the VLAN database.
Layer 3 Switching Operation and Configuration Inter-VLAN Routing with SVIs (Cont.)
Notes: 5.3.1.3 Inter-VLAN Routing with Switch Virtual Interfaces (cont)

## Slide 16: Reasons to configure SVI
To provide a gateway for a VLAN so that traffic can be routed into or out of that VLAN
To provide Layer 3 IP connectivity to the switch
To support routing protocol configurations

## Slide 17: SVI: Advantages and Disadvantages
The following are some of the advantages of SVI:
It is much faster than router-on-a-stick because everything is hardware switched and routed.
No need for external links from the switch to the router for routing.
Not limited to one link. Layer 2 EtherChannels can be used between the switches to get more bandwidth.
Latency is much lower because it does not need to leave the switch.
The following are some of the disadvantages:
It needs a Layer 3 switch to perform inter-VLAN routing, which is more expensive

## Slide 18: Routing with Routed Ports
A routed port is a physical port that acts similarly to a port on a traditional router with Layer 3 addresses configured.
Unlike an access port, a routed port is not associated with a particular VLAN. A routed port behaves like a regular router interface.
Layer 2 functionality is removed (e.g. STP).
Routed ports are used for point-to-point links.
Routed interfaces do not support subinterfaces as with Cisco IOS routers.
Configure the respective interface as a Layer 3 interface using the no switchport interface command
Notes: Layer 2 protocols are not supported e.g STP, however LACP/PAGP will still function at layer 3.
Routing convergence more deterministic and faster

## Slide 19: Routed Ports: Advantages
Following are some of the advantages of routed ports:
A multilayer switch can have SVI and routed ports in a single switch.
Multilayer switches forward either Layer 2 or Layer 3 traffic in hardware, so it helps to do routing faster.
STP domain not extended to other switches. However separate subnets are required.
Notes: No need to run STP etc
Good for point to point links.

## Slide 20: Configuring Inter-VLAN Routing Using SVI and Routed Ports

## Slide 21: Configuring Routing on a Multilayer Switch
Step 1. Create VLANs 10 and 20:
DSW1(config)# vlan 10
DSW1(config-vlan)# vlan 20
Step 2. On DSW1, enable IPv4 routing:
DSW1(config)# ip routing
Step 3. Configure SVI for VLANs with IP address
DSW1(config)# interface vlan 10
DSW1(config-if)# ip address 10.0.10.1 255.255.255.0
DSW1(config-if)# no shutdown
DSW1(config)# interface vlan 20
DSW1(config-if)# ip address 10.0.20.1 255.255.255.0
DSW1(config-if)# no shutdown

## Slide 22: Configuring Routing on a Multilayer Switch
Step 4. Turn the interface that connects to R1 (Ethernet 0/0) into a routed interface and configure it with IP address.
DSW1(config)# interface ethernet 0/2
DSW1(config-if)# no switchport
*Nov 28 15:03:55.138: %LINK-3-UPDOWN: Interface Ethernet0/2, changed state to up
*Nov 28 15:03:56.142: %LINEPROTO-5-UPDOWN: Line protocol on Interface Ethernet0/2, changed state to up
DSW1(config-if)# ip address 10.0.99.1 255.255.255.0
Step 5. Configure a Routing Protocol
DSW1(config)# router eigrp 1
DSW1(config-router)# network 10.0.0.0
*Nov 28 15:12:22.448: %DUAL-5-NBRCHANGE: EIGRP-IPv4 1: Neighbor 10.0.99.2 (Ethernet0/2) is up: new adjacency

## Slide 23: Using the SVI autostate exclude Command
The SVI interface is brought up when one Layer 2 port in the VLAN has had time to converge (transition from STP listening-learning state to forwarding state).
The default action when a VLAN has multiple ports is that the SVI goes down when all ports in the VLAN go down.
This action prevents features such as routing protocols from using the VLAN interface as if it were fully operational and minimizes other problems, such as routing black holes.
You can use the SVI autostate exclude command to configure a port so that it is not included in the SVI line-state up-and-down calculation.

## Slide 24: Configuring autostate exclude
Switch(config)# interface interface slot/number
Switch(config-if)# switchport autostate exclude
This disables the SVI autostate and makes the SVI interface permanently active.

## Slide 25
To troubleshoot Layer 3 switching issues, verify the following for accuracy:
VLANs
  VLANs must be defined across all the switches.
  VLANs must be enabled on the trunk ports.
  Ports must be in the right VLANs.
SVIs
  SVIs must have the correct IP address or subnet mask.
  SVIs must be up.
  SVIs must match with the VLAN number.
Troubleshooting Layer 3 Switching Layer 3 Switch Configuration Issues
Notes: 5.3.2.1 Layer 3 Switch Configuration Issues

## Slide 26
To troubleshoot Layer 3 switching issues, verify the following for accuracy:
Routing
  Routing must be enabled.
  Each interface or network should be added to the routing protocol.
Hosts
  Hosts must have the correct IP address or subnet mask.
  Hosts must have a default gateway associated with an SVI or routed port.
Troubleshooting Layer 3 Switching Layer 3 Switching Configuration Issues (Cont.)
Notes: 5.3.2.1 Layer 3 Switching Configuration Issues

## Slide 27
Layer 2 Versus Layer 3 EtherChannel

## Slide 28: Layer 2 Versus Layer 3 EtherChannel
On a multilayer switch, you can configure Layer 2 or Layer 3 EtherChannels, depending on what type of devices that will be connected, and depending on their position in the network.

## Slide 29: Layer 3 EtherChannel Configuration
Step 1. Create a virtual Layer 2 interface:
Switch(config)# interface port-channel 1
Step 2. Change interface to Layer 3 and enable the use of the ip address command:
Switch(config-if)# no switchport
Step 3. Assign an IP address to the port channel interface because this will now be a Layer 3 interface:
Switch(config-if)# ip address 172.32.52.10 255.255.255.0
Step 4. Navigate to the interface that is to be associated with the EtherChannel bundle.
Switch(config)# interface range fastethernet 5/4 - 5

## Slide 30: Layer 3 EtherChannel Configuration
Step 5. Remove the independent Layer 2 and Layer 3 functionality of the port so that the port can function as part of a group:
Switch(config-if-range)# no switchport
Switch(config-if-range)# channel-protocol pagp
Step 6. Assign all of the physical interfaces in the range to the EtherChannel group:
Switch(config-if-range)# channel-group 1 mode desirable

## Slide 31: L3 EtherChannel Configuration Guidelines
The following are the guidelines for configuration for EtherChannel:
Speed and duplex: Configure all interfaces in an EtherChannel to operate at the same speed and in the same duplex mode.
Interface mode: Because the port channel interface is a routed port, the no switchport the same command must also be applied to the physical ports
Verifying the EtherChannel configuration: After EtherChannel is configured, use the following commands to verify and troubleshoot EtherChannel:
show interface port-channel channel-group-number
show etherChannel channel-group-number summary
show spanning-tree vlan vlan-number detail
Notes: L3 etherchannel not working yet in VIRL (2016)