## Slide 1: Redistribution
Redistribution
Route filtering with distribution-list
Route maps

## Slide 2: Resources
OSPF Configuration Guide
http://www.cisco.com/c/en/us/td/docs/ios-xml/ios/iproute_ospf/configuration/15-mt/iro-15-mt-book.html
OSPF Design Guide
http://www.cisco.com/c/en/us/support/docs/ip/open-shortest-path-first-ospf/7039-1.html
Redistribution
http://www.cisco.com/c/en/us/support/docs/ip/enhanced-interior-gateway-routing-protocol-eigrp/8606-redist.html
http://www.cisco.com/c/en/us/support/docs/ip/open-shortest-path-first-ospf/113339-ospf-connected-net.html

## Slide 3: Redistribution
Route redistribution is when you take a route from one source (protocol) and inject it or distribute it into another protocol
E.g. Taking routes learned from RIP and advertising them via OSPF

## Slide 4: Redistributed Routes
Redistribution is always performed outbound; the router doing redistribution does not change its routing table.
The boundary router’s neighbors see the redistributed routes as external routes (OSPF, EIGRP).
Routes must be in the routing table for them to be redistributed.
Notes: As a review, remember there may be many reasons why an enterprise uses two or more interior gateway routing protocols. Whatever the reason for the change, network administrators must conduct migration from one routing protocol to another carefully and thoughtfully. The new routing protocol will most likely have different requirements and capabilities from the old one.
It is important for network administrators to understand what must be changed and to create a detailed plan before making any changes. An accurate topology map of the network and an inventory of all network devices are also critical for success.

## Slide 5: Redistribution Considerations
The key issues that arise when using redistribution:
  Routing feedback (loops)
    If more than one boundary router is performing route redistribution, then the routers might send routing information received from one autonomous system back into that same autonomous system.
  Incompatible routing information
    Each routing protocol uses different metrics to determine the best path therefore path selection using the redistributed route information might not be optimal.
  Inconsistent convergence times
    Different routing protocols converge at different rates.
Good planning should solve the majority of issues but additional configuration might be required.
  Some issues might be solved by changing the administrative distance, manipulating the metrics, and filtering using route maps, distribute lists, and prefix lists.

## Slide 6: Cisco IOS Administrative Distance
Routing Protocol | Default Administrative Distance Value
Connected interface | 0
Static route out an interface | 1
Static route to a next-hop address | 1
EIGRP summary route | 5
External BGP | 20
Internal EIGRP | 90
IGRP | 100
OSPF | 110
IS-IS | 115
RIPv1 and RIP v2 | 120
Exterior Gateway Protocol (EGP) | 140
On-Demand Routing (ODR) | 160
External EIGRP | 170
Internal BGP | 200
Unknown | 255
Trustworthiness
More
Less
Notes: Administrative Distance
Lower administrative distances are considered more believable (better).
Static routes are configured with the ip route prefix mask {address | interface-type interface-number [ip-address]} [dhcp] [distance] [name next-hop-name] [permanent | track number] [tag tag] global configuration command. If the address parameter is used in this command, specifying the address of the next-hop router to use to reach the destination network, the default administrative distance is 1. If the interface parameter is used instead, specifying the local router outbound interface to use to reach the destination network, the router considers this a directly connected route; however, the default administrative distance in this case appears to be somewhere between 0 and 1.

## Slide 7: Routing Metric
A boundary router must be capable of translating the metric of the received route into the receiving routing protocol.
  Redistributed route must have a metric appropriate for the receiving protocol.
The Cisco IOS assigns the following default metrics when a protocol is redistributed into the specified routing protocol:
Protocol That Route Is Redistributed Into … | Default Seed Metric
RIP | 0 (interpreted as infinity)
IGRP / EIGRP | 0 (interpreted as infinity)
OSPF | 20 for all except BGP routes (BGP routes have a default seed metric of 1)
IS-IS | 0
BGP | BGP metric is set to IGP metric value
Notes: A metric of infinity tells the router that the route is unreachable, and therefore, it should not be advertised. When redistributing routes into RIP, IGRP, and EIGRP, you must specify a default metric. If you do not configure a default metric, the default will be infinity which means that all routes redistributed from these three protocols will be unreachable.
For OSPF, the redistributed routes have a default type 2 metric of 20, except for redistributed BGP routes, which have a default type 2 metric of 1. For IS-IS, the redistributed routes have a default metric of 0. But unlike RIP, IGRP, or EIGRP, a seed metric of 0 will not be treated as unreachable by IS-IS. Configuring a seed metric for redistribution into IS-IS is recommended.
For BGP, the redistributed routes maintain the IGP routing metrics.

## Slide 8: Defining a Seed Metric
A seed metric, different than the default metric, can be defined during the redistribution configuration.
  After the seed metric for a redistributed route is established, the metric increments normally within the autonomous system.
    The exception to this rule is OSPF E2 routes.
Seed metrics can be defined in two ways:
  The default-metric router configuration command establishes the seed metric for all redistributed routes.
  The redistribute can also be used to define the seed metric for a specific protocol.

## Slide 9: OSPF Seed Metric Example #1
R3(config)# router rip
R3(config-router)# network 172.18.0.0
R3(config-router)# network 172.19.0.0
R3(config-router)# router ospf 1
R3(config-router)# network 192.168.2.0 0.0.0.255 area 0
R3(config-router)# redistribute rip subnets metric 30
R3(config-router)#
172.16.0.0
172.17.0.0
172.20.0.0
172.19.0.0
172.18.0.0
192.168.2.0
Cost = 10
Cost = 100
RIP AS
OSPF
R1
R2
R3
R4
C 172.16.0.0
C 172.20.0.0
R [120/1] 172.17.0.0
R [120/1] 172.19.0.0
R [120/2] 172.18.0.0
Table R1
C 172.17.0.0
C 172.19.0.0
C 172.20.0.0
R [120/1] 172.16.0.0
R [120/1] 172.18.0.0
Table R2
C 172.18.0.0
C 172.19.0.0
R [120/1] 172.17.0.0
R [120/1] 172.20.0.0
R [120/2] 172.16.0.0
C 192.168.2.0
O [110/110] 192.168.1.0
Table R3
C 192.168.1.0
C 192.168.2.0
O E2 [110/30] 172.16.0.0
O E2 [110/30] 172.17.0.0
O E2 [110/30] 172.18.0.0
O E2 [110/30] 172.19.0.0
O E2 [110/30] 172.20.0.0
Table R4
192.168.4.0
Notes: As we know, each routing protocol defines a metric for each route. When a router redistributes routes from one routing domain to another this information cannot be translated from one routing protocol to another. A RIP hop cannot be dynamically recalculated to an OSPF cost by the router doing redistribution.
Therefore, a seed metric is used to artificially set the distance, cost, etc., to each external (redistributed) network from the redistribution point.
For example, OSPF has been defined to make the seed metric for redistributed RIP routes to be 30.
  If the link cost of the Serial link to R4 is 100. The routes are redistributed as E2 routes, so the cost for networks 172.16.0.0, 172.17.0.0, and 172.18.0.0 in R4 is only the seed metric (30).
  Notice that the metrics of the three networks in the RIP cloud are irrelevant in the OSPF cloud because the router in the OSPF network (R4) forwards any traffic for these three networks to the border (redistributing) router, R3. R3 then forwards the traffic within the RIP network appropriately.

## Slide 10: OSPF Seed Metric Example #2
R3(config)# router rip
R3(config-router)# network 172.18.0.0
R3(config-router)# network 172.19.0.0
R3(config-router)# router ospf 1
R3(config-router)# network 192.168.2.0 0.0.0.255 area 0
R3(config-router)# redistribute rip subnets
R3(config-router)# default-metric 30
172.16.0.0
172.17.0.0
172.20.0.0
172.19.0.0
172.18.0.0
192.168.2.0
Cost = 10
Cost = 100
RIP AS
OSPF
R1
R2
R3
R4
C 172.16.0.0
C 172.20.0.0
R [120/1] 172.17.0.0
R [120/1] 172.19.0.0
R [120/2] 172.18.0.0
Table R1
C 172.17.0.0
C 172.19.0.0
C 172.20.0.0
R [120/1] 172.16.0.0
R [120/1] 172.18.0.0
Table R2
C 172.18.0.0
C 172.19.0.0
R [120/1] 172.17.0.0
R [120/1] 172.20.0.0
R [120/2] 172.16.0.0
C 192.168.2.0
O [110/110] 192.168.1.0
Table R3
C 192.168.1.0
C 192.168.2.0
O E2 [110/30] 172.16.0.0
O E2 [110/30] 172.17.0.0
O E2 [110/30] 172.18.0.0
O E2 [110/30] 172.19.0.0
O E2 [110/30] 172.20.0.0
Table R4
192.168.4.0

## Slide 11: One-Point Redistribution
One-point redistribution can be configured in either:
  One-point One-way
    Redistributes networks from one routing protocol into the other routing protocol.
    Typically uses a default or static route so that devices in that other part of the network can reach the first part of the network.
  One-point Two-way
    Redistributes routes between the two routing processes, in both directions.
RIP
OSPF
One-Point One-Way Redistribution
Redistributing from RIP to OSPF
RIP
OSPF
One-Point Two-Way Redistribution
Redistributing from RIP to OSPF
and from OSPF to RIP
Default route to the OSPF network
Notes: In the one-point, one-way redistribution example, the OSPF domain would have knowledge of the RIP routes. However the RIP domain would require a static route to reach the OSPF domain.
In the one-point, two-way redistribution example, the RIP domain would know the OSPF networks, and the OSPF domain would know the RIP routes.

## Slide 12: One-Point One-Way Redistribution Issue
OSPF
Although one-point one-way or two-way redistribution is usually safe from routing loops, issues can still occur if multiple boundary routers exist and only one router is performing one-point one-way redistribution.
  In this example, R2 is redistributing an external EIGRP route into the OSPF domain.
R2
R3
R1
EIGRP
R1 announces the external EIGRP route 10.0.0.0 with an administrative distance of 170 to both R2 and R3.
Only R2 is configured to redistribute the EIGRP routes into the OSPF domain.
Therefore the external 10.0.0.0 network is redistributed into the OSPF domain with an administrative distance of 110.
O E2 10.0.0.0/8 [110/20]
Although R3 has a direct connection to R1, R3 will use the OSPF route via R2 to get to the 10.0.0.0 network due to the lower administrative distance of OSPF (110).
This creates a suboptimal routing issue.
D EX 10.0.0.0/8 [170/41024000]
D EX 10.0.0.0/8 [170/41024000]
1
2
3
Notes: The following example displays how one-point one-way redistribution can result in suboptimal routing .
Router R1 running EIGRP is announcing an external route to routers R2 and R3.
Both of these routers are running the two routing protocols OSPF and EIGRP, but the redistribution between EIGRP and OSPF only occurs on router R2.
Router R3 receives routing update information for the external route directly from router R1 via EIGRP, and via OSPF from router R2.
The administrative distance of OSPF (110) is lower than administrative distance of external EIGRP routes (170), so router R3 selects the OSPF route.
Instead of sending packets directly from router R3 to router R1, router R3 prefers the path via router R2, resulting in suboptimal routing.

## Slide 13: Multipoint Redistribution
Multipoint redistribution has two (or more) separate routers running both routing protocols.
Redistribution can be configured as:
  Multipoint one-way redistribution
  Multipoint two-way redistribution
  Although multipoint two-way redistribution is especially problematic, either method is likely to introduce potential routing feedback loops.
RIP
OSPF
Multipoint One-Way Redistribution
Redistributing RIP into OSPF
RIP
OSPF
Multipoint Two-Way Redistribution
Redistributing RIP into OSPF and OSPF into RIP
Redistributing RIP into OSPF
Redistributing RIP into OSPF and OSPF into RIP

## Slide 14: Multipoint Redistribution
Routing Protocol A
Multipoint one-way redistribution only works well if:
  The receiving routing protocol is either EIGRP, BGP and OSPF because they support different administrative distances for internal and external routes.
  The administrative distance of protocol B’s external routes is higher than the administrative distance of protocol A’s routes, so that R2 and R3 will use the appropriate routes to destinations in the protocol A side of the network.
R2
R3
R1
Routing Protocol B
R1 announces protocol B routes to both R2 and R3.
R2 is configured to redistribute routing protocol B routes.
R3 is configured to redistribute routing protocol B routes.
Protocol B routes
Protocol B routes
1
2
3
Redistributed protocol B routes

## Slide 15: Preventing Routing Loops
The safest way to perform redistribution is to redistribute routes in only one direction, on only one boundary router within the network.
  However, this results in a single point of failure in the network.
If redistribution must be done in both directions or on multiple boundary routers, the redistribution should be tuned to avoid problems such as suboptimal routing and routing loops.

## Slide 16: Redistribution Guidelines
Do not overlap routing protocols.
  Do not run two different protocols in the same Internetwork.
  Instead, have distinct boundaries between networks that use different routing protocols.
Be familiar with your network.
  Knowing the network will result in the best decision being made.

## Slide 17: Redistributing into RIP
Redistribute routes into RIP.
Router(config-router)#
redistribute protocol [process-id] [match route-type] [metric metric-value] [route-map map-tag]
Parameter | Description
protocol | The source protocol from which routes are redistributed.
process-id | For OSPF, this value is an OSPF process ID. For EIGRP or BGP, this value is an AS number. This parameter is not required for IS-IS.
route-type | (Optional) A parameter used when redistributing OSPF routes into another routing protocol.
metric-value | (Optional) A parameter used to specify the RIP hop count seed metric for the redistributed route. If this value is not specified and no value is specified using the default-metric router configuration command, then the default metric is 0 and interpreted as infinity which means that routes will not be redistributed.
map-tag | (Optional) Specifies the identifier of a configured route map to be interrogated to filter the importation of routes from the source routing protocol to the current RIP routing protocol.
Notes: A metric-value must be specified or the default-metric command must be configured. A metric configured in a redistribute command overrides the value in the default-metric command for that one protocol.

## Slide 18: Redistributing into RIP Example
R1(config)# router rip
R1(config-router)# redistribute ospf 1 metric 3
R1(config-router)#
C 10.1.1.0
R 192.168.1.0 [120/1]
0 172.16.1.0 [110/50]
Table R1
C 10.1.1.0
C 192.168.1.0
R 172.16.0.0 [120/3]
Table R2
R1
.2
Fa0/0
10.1.1.0 /24
OSPF
RIP
.1
Fa0/0
O 172.16.1.0/24 [110/50]
R 172.16.0.0 [120/3]
192.168.1.0 /24
R2
Notes: On R1, routes from OSPF process 1 are redistributed into RIP and are given a seed metric of 3. Because no route type is specified, both internal and external OSPF routes are redistributed into RIP.
R2 learns about the 172.16.0.0 network from R1 via RIP; R2’s routing table has 172.16.0.0 installed as a RIP route. Notice that the route is automatically summarized by R1.

## Slide 19: Redistributing into OSPF
Redistribute routes into OSPF.
Router(config-router)#
redistribute protocol [process-id] [metric metric-value] [metric-type type-value] [route-map map-tag] [subnets] [tag tag-value]
Parameter | Description
protocol | The source protocol from which routes are redistributed.
process-id | For EIGRP or BGP, this value is an AS number. This parameter is not required for RIP or IS-IS.
metric-value | (Optional) A parameter that specifies the OSPF seed metric used for the redistributed route. The default metric is a cost of 20 (except for BGP routes, which have a default metric of 1).
map-tag | (Optional) Specifies the identifier of a configured route map to be interrogated to filter the importation of routes from the source routing protocol to the current OSPF routing protocol.
subnets | (Optional) OSPF parameter that specifies that subnetted routes should be redistributed. Otherwise, only classful routes are redistributed.
tag-value | (Optional) A 32-bit decimal value attached to each external route to be used by ASBRs.
Notes: A metric configured in a redistribute command overrides the value in the default-metric command for that one protocol.
Metric-type = 1 or 2 (E1 or E2) 1 = cumulative

## Slide 20: Redistributing into OSPF Example
R1(config)# router ospf 1
R1(config-router)# redistribute eigrp 100 subnets metric-type 1
R1(config-router)#
C 10.1.1.0
0 192.168.1.0 [110/20]
D 172.16.1.0 [90/409600]
Table R1
C 10.1.1.0
C 192.168.1.0
O E1 172.16.1.0 [110/20]
Table R2
R1
.2
Fa0/0
10.1.1.0 /24
EIGRP AS 100
OSPF
.1
Fa0/0
D 172.16.1.0/24 [90/409600]
O E1 172.16.1.0 [110/20]
192.168.1.0 /24
R2
Notes: Note that the subnets keyword is used so subnets are redistributed. If this keyword were omitted, no subnets would be redistributed into the OSPF domain (including the 172.16.1.0 subnet).
Omitting the subnets keyword is a common configuration error.
Also notice that a metric value is optional since OSPF will automatically assign a cost of 20 and identify the route as an E2 type route.

## Slide 21: Modifying the Administrative Distance
When routes are redistributed between two different routing protocols, some information may be lost making route selection more confusing.
One approach to correct this is to control the administrative distance to indicate route selection preference and ensure that route selection is unambiguous.
  Although, this approach does not always guarantee the best route is selected, only that route selection will be consistent.
For all protocols use the distance administrative-distance router configuration command.
  Alternatively for OSPF, use the distance ospf command.
  Alternatively for EIGRP, use the distance eigrp command.
Notes: You should change the default administrative distance carefully and by considering the network’s specific requirements.

## Slide 22: Modifying OSPF Administrative Distance
Change the default administrative distances of OSPF.
Router(config-router)#
distance ospf {[intra-area dist1] [inter-area dist2] [external dist3]
Parameter | Description
dist1 | (Optional) Specifies the administrative distance for all OSPF routes within an area. Acceptable values are from 1 to 255 while the default is 110.
dist2 | (Optional) Specifies the administrative distance for all OSPF routes from one area to another area. Acceptable values are from 1 to 255 while the default is 110.
dist3 | (Optional) Specifies the administrative distance for all routes from other routing domains, learned by redistribution. Acceptable values are from 1 to 255 while the default is 110.

## Slide 23: Redistribution Sources
Routing protocol (rip, ospf, eigrp, bgp)
Directly connected networks
router ospf 1
redistribute connected subnets metric 1
Static routes
router ospf 1
redistribute static subnets metric 1

## Slide 24: ROUTE FILTERING

## Slide 25: Using Distribute Lists
One way to control routing updates is to use a distribute list which allows an ACL to be applied to routing updates for filtering purposes.
  Administrators control which routes get distributed.
  This control is for security, overhead, and management reasons.
It’s important to understanding that the distribution lists are used to control (filter) routing updates while ACLs filter user traffic.
Sample implementation plan:
  Identify network traffic to be filtered using an ACL or route map.
  Associate the distribute list with the ACL or route-map using the distribute-list router configuration command.
Notes: Access lists are usually associated with interfaces and are usually used to control user traffic (data plane traffic) rather than routing protocol traffic (or other control plane traffic).
However, routers can have many interfaces, and route information can also be obtained through route redistribution, which does not involve a specific interface.
In addition, access lists do not affect traffic originated by the router, so applying one on an interface has no effect on outgoing routing advertisements.
However, when you configure an access list and use it with a distribute list, routing updates can be controlled, no matter what their source is.

## Slide 26: Filter Outgoing Routing Updates Example 1a
R2(config)# access-list 7 permit 172.16.0.0 0.0.255.255
R2(config)#
R2(config)# router eigrp 1
R2(config-router)# network 172.16.0.0
R2(config-router)# network 192.168.5.0
R2(config-router)# distribute-list 7 out Serial0/0/0
R2(config-router)#
In this example, the network 10.0.0.0 must be hidden from the devices in network 192.168.5.0.
  The distribute-list out command on R2 applies ACL 7 to packets going out S0/0/0 which only permits 172.16.0.0 routing information to be distributed out.
  The implicit deny any at the end of the ACL prevents updates about any other networks from being advertised and as a result, network 10.0.0.0 is hidden.
10.0.0.0
172.16.0.0
192.168.5.0
EIGRP AS 1
R1
R2
R3
D 10.0.0.0/8 [90/...]
S0/0/0
D 172.16.0.0/16 [90/...]
D 10.0.0.0/8 [90/...]

## Slide 27: Filter Outgoing Routing Updates Example 1b
R2(config)# access-list 7 deny 10.0.0.0 0.255.255.255
R2(config)# access-list 7 permit any
R2(config)#
R2(config)# router eigrp 1
R2(config-router)# network 172.16.0.0
R2(config-router)# network 192.168.5.0
R2(config-router)# distribute-list 7 out Serial0/0/0
R2(config-router)#
As an alternative, network 10.0.0.0 can be explicitly denied and all other routes are valid.
  The distribute-list out command on R2 applies ACL 7 to packets going out S0/0/0 which denies the 10.0.0.0/8 network but permits all other routes.
10.0.0.0
172.16.0.0
192.168.5.0
EIGRP AS 1
R1
R2
R3
D 10.0.0.0/8 [90/...]
S0/0/0
D 172.16.0.0/16 [90/...]
D 10.0.0.0/8 [90/...]

## Slide 28: OSPF Filtering considerations
Filtering information with link-state protocols such as OSPF is challenging.
Distribute-list out works on the ASBR to filter redistributed routes into other protocols.
Distribute-list in works on any router to prevent routes from being put in the routing table, but it does not prevent link-state packets from being propagated, downstream routers would still have the routes.
Avoid OSPF filtering as much as possible if filters can be applied on the other protocols to prevent loops.

## Slide 29: Understanding Route Maps
Route maps are similar in function to ACLs, but provide far more control.
Route maps are more similar to a scripting language.
  They can be named rather than numbered for easier documentation.
  Lines are sequence-numbered for easier editing.
  Match and set criteria can be used, similar to the “if, then” logic.
    They allow conditions to be tested using match commands and if the conditions match, actions specified by set commands can be taken to modify attributes of the packet or routes.
Just as ACLs are used by a variety of Cisco IOS features, route maps can also be used for various applications.
  The actual route map implementation will vary based on how its applied.

## Slide 30: Route Map Applications
Route filtering during redistribution
  All IP routing protocols can use route maps for redistribution filtering.
  Applied using the redistribute protocol route-map router configuration command.
Policy-based routing (PBR)
  PBR allows the operator to define routing policy other than basic destination-based routing using the routing table.
  Applied using the ip policy route-map interface configuration command.
NAT
  Route maps provide more control over which private addresses are translated to public addresses.
BGP
  Route maps are the primary tools for implementing BGP policy.
Notes: Route filtering during redistribution—Redistribution nearly always requires some amount of route filtering. Although distribute lists can be used for this purpose, route maps offer the added benefit of manipulating routing metrics through the use of set commands.
Policy-based routing (PBR)—Route maps can be used to match source and destination addresses, protocol types, and end-user applications. When a match occurs, a set command can be used to define the interface or next-hop address to which the packet should be sent. PBR allows the operator to define routing policy other than basic destination-based routing using the routing table.
NAT—Route maps can better control which private addresses are translated to public addresses. Using a route map with NAT also provides more detailed show commands that describe the address-translation process.
BGP—Route maps are the primary tools for implementing BGP policy. Network administrators assign route maps to specific BGP sessions (neighbors) to control which routes are allowed to flow in and out of the BGP process. In addition to filtering, route maps provide sophisticated manipulation of BGP path attributes. Route maps for BGP are discussed in Chapter 6, “Implementing a BGP Solution for ISP Connectivity.”

## Slide 31: Defining a Route Map
Define a route map and enter route map configuration mode.
Router(config)#
route-map map-tag [permit | deny] [sequence-number]
Each route map statement is numbered by a sequence number and for this reason can be edited.
The default for the route-map command is permit, with a sequence-number of 10.
Parameter | Description
map-tag | Name of the route map.
permit ¦ deny | (Optional) A parameter that specifies the action to be taken if the route map match conditions are met; the meaning of permit or deny is dependent on how the route map is used.
sequence-number | (Optional) A sequence number that indicates the position that a new route map statement will have in the list of route map statements already configured with the same name.
Notes: When the sequence-number parameter of the route-map command is not used, the following occurs:
If no other entry is already defined with the supplied route-map tag, an entry is created, with the sequence-number set to 10.
If only one entry is already defined with the supplied route-map tag, that entry is the default entry for the route-map command, and the sequence-number of the entry is unchanged. (The router assumes you are editing the one entry that is already defined.)
If more than one entry is already defined with the supplied route-map tag, an error message is displayed, indicating that the sequence-number is required.
If the no route-map map-tag command is specified (without the sequence-number parameter), then the whole route map is deleted.

## Slide 32: Route Map Operation Logic
A route map consists of a list of statements.
  The list is processed top-down like an access list.
  Sequence numbers are used for inserting or deleting specific statements.
Route map permit or deny determines if the candidate will be redistributed.
  At least one reference must permit the route for it to be a candidate for redistribution.
The first match found for a route is applied.
  The match statement may contain multiple references.
    Multiple match criteria in the same line use a logical OR.
    Multiple match criteria in multiple separate lines use a logical AND.
  Once there is a match, set the action (if defined) and leave the route map.
    Other route-map statements are not processed.
Notes: Matching statements in a route map can be complex. Multiple match criteria in the same line are processed with OR logic. Separate match criteria can also be applied vertically under a route map line. In this case, each match uses AND logic.
A route map may consist of multiple route map statements. The statements are processed top-down, like an ACL. The first match found for a route is applied. The sequence number is used for inserting or deleting specific route map statements in a specific place in the route map.
The match route map configuration commands define the conditions to be checked. The set route map configuration commands define the actions that you should follow if there is a match.
The single-match statement may contain multiple conditions. At least one condition in the match statement must be true to consider the statement a match (logical OR). A route map statement may contain multiple match statements. All match statements in the route map statement must be true to consider the route map statement a match (logical AND).
The sequence number specifies the order in which conditions are checked. For example, if there are two statements in a route map named MYMAP, one with sequence 10 and the other with sequence 20, sequence 10 is checked first. If the match conditions in sequence 10 are not met, then sequence 20 is checked.
Like an ACL, there is an implicit deny any at the end of a route map. The consequences of this deny depend on how the route map is used.

## Slide 33: Route Map Operation Example
Match criteria on the same line mean a logical OR condition (If this or this or …).
Multiple match and set criteria on separate lines indicates an AND condition (and if this …).
A route-map statement without any match statements will be considered matched.
Like an access list, an implicit deny any appears at the end of a route map.
  The consequences of this deny depend on how the route map is being used.
route-map DEMO permit 10
match X Y Z
match A
set B
set C
route-map DEMO permit 20
match Q
set R
route-map DEMO permit 30
If {(X OR Y OR Z)
AND A match}
Then {Set B AND C}
(and exit route-map)
Else
If Q matches
Then set R (and exit route-map)
Else
Set nothing (and exit route-map)
OR
AND
AND
Notes: The following is a simple example to see how route-map statements would be interpreted.
Each route-map statement is attributed a sequence for editing purposes.
Match criteria on the same line mean a logical OR condition.
Match criteria on separate lines indicates an AND condition.
Note that on a router, all the conditions and actions shown would be replaced with specific conditions and actions, depending on the exact match and set commands used.
A route-map statement without any match statements will be considered matched.

## Slide 34: The match Commands
Command | Description
match community | Matches a BGP community
match interface | Matches any routes that have the next hop out of one of the interfaces specified
match ip address | Matches any routes that have a destination network number address that is permitted by a standard or extended ACL
match ip next-hop | Matches any routes that have a next-hop router address that is passed by one of the ACLs specified
match ip route-source | Matches routes that have been advertised by routers and access servers at the address that is specified by the ACLs
match length | Matches based on the layer 3 length of a packet
match metric | Matches routes with the metric specified
match route-type | Matches routes of the specified type
match tag | Matches tag of a route
Notes: The table presents a general list of match criteria. Some criteria are used for BGP policy, some criteria are used for policy-based routing, and some criteria are used for redistribution filtering.

## Slide 35: The set Commands
Command | Description
set as-path | Modifies an AS path for BGP routes
set automatic-tag | Computes automatically the tag value
set community | Sets the BGP communities attribute
set default interface | Indicates where to output packets that pass a match clause of a route map for policy routing and have no explicit route to the destination
set interface | Indicates where to output packets that pass a match clause of a route map for policy routing
set ip default next-hop | Indicates where to output packets that pass a match clause of a route map for policy routing and for which the Cisco IOS software has no explicit route to a destination
set ip next-hop | Indicates where to output packets that pass a match clause of a route map for policy routing
set level | Indicates where to import routes for IS-IS and OSPF
set local-preference | Specifies a BGP local preference value
set metric | Sets the metric value for a routing protocol
set metric-type | Sets the metric type for the destination routing protocol
set tag | Sets tag value for destination routing protocol
set weight | Specifies the BGP weight value
Notes: Not all the set options are listed here and not all of the ones listed are used for redistribution purposes. The table includes options for BGP and policy-based routing.

## Slide 36: Configuring Route Maps for Redistribution
Use route maps when you want detailed control over how routes are redistributed between routing protocols.
Sample implementation plan:
  Define and name the route map with the route-map command.
    Define the conditions to match (the match statements).
    Define the action to be taken when there is a match (the set statements).
  Specify the route map to use when redistributing.
    Use the redistribute protocol route-map map-tag router configuration command.
Notes: Note: When route maps are used for redistribution, the route maps are applied to the redistribute router configuration command.
PBR is covered in more detail in chapter 5.

## Slide 37: route-map Commands for Redistribution
redistribute protocol [process-id] route-map map-tag
Router(config-router)#
Allows for detailed control of routes being redistributed into a routing protocol.
route-map map-tag [permit | deny] [sequence-number]
Router(config)#
Defines the route map conditions.
match {conditions}
Router(config-route-map)#
Defines the conditions to match.
set {actions}
Router(config-route-map)#
Defines the action to be taken on a match.
Notes: This slide shows the parameters for the route-map commands.
map-tag: Specifies the name of the route map
permit | deny: Specifies the action to be taken if the route map match conditions are met
  permit = permit the matched route to be redistributed
  deny = deny the matched route from being redistributed
sequence-number: Specifies the sequence number that indicates the position that a new route map statement will have in the list of route map statements already configured with the same route map name
When used for redistribution filtering, a route map is applied to the route redistribution process by adding the route-map command and map-tag to the end of the redistribute protocol command.
Implicit deny all at end of route map

## Slide 38: Configuring Route Maps for Redistribution
The route map REDIS-RIP tests the following;
  In sequence 10, any routes matching ACLs 23 or 29 will have their metric changed accordingly.
  In sequence 20, any routes matching ACLs 37 will not be redistributed.
  In sequence 30, all other routes will have their metric changed accordingly.
Finally, all RIP routes and subnets will be redistributed into OSPF according to the REDIS-RIP route map statements.
R1(config)# access-list 23 permit 10.1.0.0 0.0.255.255
R1(config)# access-list 29 permit 172.16.1.0 0.0.0.255
R1(config)# access-list 37 permit 10.0.0.0 0.255.255.255
R1(config)#
R1(config)# route-map REDIS-RIP permit 10
R1(config-route-map)# match ip address 23 29
R1(config-route-map)# set metric 500
R1(config-route-map)# set metric-type type-1
R1(config-route-map)#
R1(config-route-map)# route-map REDIS-RIP deny 20
R1(config-route-map)# match ip address 37
R1(config-route-map)#
R1(config-route-map)# route-map REDIS-RIP permit 30
R1(config-route-map)# set metric 5000
R1(config-route-map)# set metric-type type-2
R1(config-route-map)#
R1(config-route-map)# router ospf 10
R1(config-router)# redistribute rip route-map REDIS-RIP subnets
R1(config-router)#
Notes: Sequence number 10 of the route map is looking for an IP address match in access list 23 or access list 29.
  Routes 10.1.0.0/16 and 172.16.1.0/24 match these lists.
  If a match is found, the router redistributes the route into OSPF with a cost metric of 500 and sets the new OSPF route to external type 1.
If there is no match to sequence number 10, sequence number 20 is checked.
  If there is a match in access list 37 (10.0.0.0/8), that route is not redistributed into OSPF, because sequence number 20 specifies deny.
If there is no match to sequence number 20, sequence number 30 is checked.
  Because sequence number 30 is a permit and there is no match criterion, all remaining routes are redistributed into OSPF with a cost metric of 5000 and an external metric of type 2.
Note that the decision of whether to redistribute a route or not is based on the deny or permit in the route-map command, and not the deny or permit in the ACLs referenced by the route-map command. The ACLs are used only to match routes in the route-map statements.
The ACL permits or denies routes to be processed by the route-map

## Slide 39: Route Maps to Avoid Route Feedback
R1(config)# access-list 1 permit 192.168.1.0 0.0.0.255
R1(config)# route-map OSPF-into-RIP deny 10
R1(config-route-map)# match ip address 1
R1(config-route-map)# route-map OSPF-into-RIP permit 20
R1(config-route-map)# router rip
R1(config-router)# redistribute ospf 10 metric 5 route-map OSPF-into-RIP
R1(config-router)# router ospf 10
R1(config-router)# redistribute rip subnets
R1(config-router)#
To prevent the routing feedback loop, a route map called OSPF-into-RIP has been applied to R1 and R2.
  In sequence 10, any routes matching ACL 1 is denied and will not be redistributed back into RIP.
  In sequence 20, all other routes are permitted to be redistributed and will be assigned a RIP metric of 5.
RIPv2
OSPF Area 0
O E2 192.168.1.0 [110/20]
O E2 192.168.1.0 [110/20]
R1
R2
R 192.168.1.0 [120/1]
R3