## Slide 1: IN723 BGP Lesson 3
Update source
eBGP multihop
Next-hop self
Synchronisation
Troubleshooting
Originating a route
Route maps
Redistribution
Setting attributes

## Slide 2: Resources
Case Studies
http://www.cisco.com/c/en/us/support/docs/ip/border-gateway-protocol-bgp/26634-bgp-toc.html
Configuration Guide
http://www.cisco.com/c/en/us/td/docs/ios-xml/ios/iproute_bgp/configuration/15-mt/irg-15-mt-book.html
Command Reference
http://www.cisco.com/c/en/us/td/docs/ios-xml/ios/iproute_bgp/command/irg-cr-book.html
Notes: Microsegmentation = split a larger collision domain into smaller ones in order to reduce collision probability

## Slide 3: IBGP Source IP Address Problem
BGP does not accept unsolicited updates.
  It must be aware of every neighboring router and have a neighbor statement for it.
For example, when a router creates and forwards a packet, the IP address of the outbound interface is used as that packet’s source address by default.
  For BGP packets, this source IP address must match the address in the corresponding neighbor statement on the other router or the routers will not establish the BGP session.
  This is not a problem for EBGP neighbors as they are typically directly connected.

## Slide 4: IBGP Source IP Address Problem
When multiple paths exist between IBGP neighbors, the BGP source address can cause problems:
  Router D uses the neighbor 10.3.3.1 remote-as 65102 command to establish a relationship with A.
  However, router A is sending BGP packets to D via B therefore the source IP address of the packets is 10.1.1.1.
  The IBGP session between A and D cannot be established because D does not recognize 10.1.1.1 as a BGP neighbor.

## Slide 5: IBGP Source IP Address Solution
Establish the IBGP session using a loopback interface.
Router(config-router)#
neighbor {ip-address | peer-group-name} update-source loopback interface-number
Informs the router to use a loopback interface address for all BGP packets.
Overrides the default source IP address for BGP packets.
Typically only used with IBGP sessions.
As an added bonus, physical interfaces can go down for any number of reasons but loopbacks never fail.
Notes: The update-source option in the neighbor command overrides the default source IP address used for BGP packets. It is necessary to tell the router which IP address to use as the source address for all BGP packets if you want to use a loopback interface instead of the physical interface.
If you do not use the update-source option in the neighbor command, an announcement going to a neighbor uses the IP address of the exiting interface as the source address for a packet. When a router creates a packet, whether it is a routing update, a ping, or any other type of IP packet, the router does a lookup in the routing table for the destination address. The routing table lists the appropriate interface to get to the destination address. The address of this outbound interface is used as the source address of that packet by default.
Consider what would happen if a neighboring router uses the loopback interface address in its neighbor command for this router, but you do not use the neighbor update-source command on this router. When the neighboring router receives an update packet and looks at the source address of the packet, it sees that it has no neighbor relationship with that source address, so it discards the packet.
BGP does not accept unsolicited updates; it must be aware of every neighboring router and have a neighbor statement for it.

## Slide 6: IBGP Source IP Address Example
AS 65102
AS 65100
R1
R4
Lo0 192.168.2.2
.1
192.168.1.1
172.16.1.1
R2
R3
10.1.1.0/24
10.2.2.0/24
.1
.2
.2
Lo0 192.168.3.3
AS 65101
OSPF
R2(config)# router bgp 65101
R2(config-router)# neighbor 172.16.1.1 remote-as 65100
R2(config-router)# neighbor 192.168.3.3 remote-as 65101
R2(config-router)# neighbor 192.168.3.3 update-source loopback0
R2(config-router)# exit
R2(config)# router ospf 1
R2(config-router)# network 10.0.0.0 0.0.0.0 area 0
R2(config-router)# network 192.168.2.0 area 0
R2(config-router)#
R3(config)# router bgp 65101
R3(config-router)# neighbor 192.168.1.1 remote-as 65102
R3(config-router)# neighbor 192.168.2.2 remote-as 65101
R3(config-router)# neighbor 192.168.2.2 update-source loopback0
R3(config-router)# exit
R3(config)# router ospf 1
R3(config-router)# network 10.0.0.0 0.0.0.0 area 0
R3(config-router)# network 192.168.3.0 0.0.0.0 area 0
R3(config-router)#
Notes: Notice the IGP must now advertise the loopbacks as well.

## Slide 7: EBGP Dual-Homed Problem
R1 in AS 65102 is dual-homed with R2 in AS 65101.
A problem can occur if R1 only uses a single neighbor statement pointing to 192.168.1.18 on R2 .
  If that link fails, the BGP session between these AS is lost, and no packets pass from one autonomous system to the next, even though another link exists.
A solution is configuring two neighbor statements on R1 pointing to 192.168.1.18 and 192.168.1.34.
  However, this doubles the BGP updates from R1 to R2.

## Slide 8: EBGP Dual-Homed Solution
The ideal solution is to:
  Use loopback addresses.
  Configure static routes to reach the loopback address of the other router.
  Configure the neighbor ebgp-multihop command to inform the BGP process that this neighbor is more than one hop away.

## Slide 9: Enable Multihop EBGP
Increase the time-to-live (TTL) for EBGP connections.
Router(config-router)#
neighbor {ip-address | peer-group-name} ebgp-multihop [ttl]
This command is of value when redundant paths exist between EBGP neighbors.
The default ttl is 1, therefore BGP peers must be directly connected.
  The range is from 1 to 255 hops.
Increasing the ttl enables BGP to establish EBGP connections beyond one hop and also enables BGP to perform load balancing.
Notes: When an EBGP router is peering with an external neighbor, the only address that it can reach without further configuration is the interface that is directly connected to that EBGP router. Because internal routing information is not exchanged with external peers, the router has to point to a directly connected address for that external neighbor.
A loopback interface is never directly connected. Therefore, if you want to use a loopback interface instead, use static routes pointing at the physical address of the directly connected network (the next-hop address). In addition to the static route, you need to use the neighbor ip-address ebgp-multihop [ttl] router configuration command.
This command allows the router to accept and attempt BGP connections to external peers residing on networks that are not directly connected. This command increases the default of one hop for EBGP peers by changing the default Time to Live (TTL) value of 1. It allows routes to the EBGP loopback address with a hop value greater than 1. By default, the TTL is set to 255 with this command. This command is of value when redundant paths exist between EBGP neighbors.

## Slide 10: Multihop EBGP Example
AS 65102
Lo0 172.17.1.1
R1
R2
EBGP
EBGP
192.168.1.18 /28
Lo0 172.16.1.1
AS 65101
192.168.1. 34 /28
192.168.1.17 /28
192.168.1. 33 /28
R1(config)# router bgp 65102
R1(config-router)# neighbor 172.16.1.1 remote-as 65101
R1(config-router)# neighbor 172.16.1.1 update-source loopback0
R1(config-router)# neighbor 172.16.1.1 ebgp-multihop 2
R1(config-router)# exit
R1(config)# ip route 172.16.1.1 255.255.255.255 192.168.1.18
R1(config)# ip route 172.16.1.1 255.255.255.255 192.168.1.34
R1(config)#
R2(config)# router bgp 65101
R2(config-router)# neighbor 172.17.1.1 remote-as 65102
R2(config-router)# neighbor 172.17.1.1 update-source loopback0
R2(config-router)# neighbor 172.17.1.1 ebgp-multihop 2
R2(config-router)# exit
R2(config)# ip route 172.17.1.1 255.255.255.255 192.168.1.17
R2(config)# ip route 172.17.1.1 255.255.255.255 192.168.1.33
R2(config)#
Notes: In these examples, the commands used on R1 and R2 inform BGP that the neighbor address is two hops away (one hop to the other router and one hop through the router to the loopback interface).
Note:
  Recall that BGP is not designed to perform load balancing. Paths are chosen because of policy, not based on bandwidth. BGP will choose only a single best path.
  Using the loopback addresses and the neighbor ebgp-multihop command allows load balancing, and redundancy, across the two paths between the AS.

## Slide 11: Advertising EBGP Routes to IBGP Peers
When an EBGP router receives an update from an EBGP neighbor and forwards the update to its IBGP peers, the source IP address will still be that of the EBGP router.
  IBGP neighbors will have to be configured to reach that external IP address.
Another solution is to override a router’s default behavior and force it to advertise itself as the next-hop address for routes sent to a neighbor.
  To do so, use the neighbor next-hop-self router configuration command
  Note: The next-hop is advertised unchanged to IBGP peers

## Slide 12: neighbor next-hop-self Command
Configure the router as the next hop for a BGP-speaking peer.
Router(config-router)#
neighbor {ip-address | peer-group-name} next-hop-self
The command forces BGP to advertise itself as the source of the routes.
The ip-address identifies the peer router to which advertisements will be sent, with this router identified as the next hop.
This command is useful in unmeshed networks (such as Frame Relay) where BGP neighbors may not have direct access to all other neighbors on the same IP subnet.

## Slide 13: Next Hop Self Example
R2(config)# router bgp 65101
R2(config-router)# neighbor 172.16.1.1 remote-as 65100
R2(config-router)# neighbor 192.168.3.3 remote-as 65101
R2(config-router)# neighbor 192.168.3.3 update-source loopback0
R2(config-router)# neighbor 192.168.3.3 next-hop-self
R2(config-router)# exit
R2(config)# router eigrp 1
R2(config-router)# network 10.0.0.0
R2(config-router)# network 192.168.2.0
R2(config-router)#
AS 65102
AS 65100
R1
R4
Lo0 192.168.2.2
.1
192.168.1.1
172.16.1.1
R2
R3
10.1.1.0/24
10.2.2.0/24
.1
.2
.2
Lo0 192.168.3.3
AS 65101
EIGRP
Notes: R2 uses the neighbor next-hop-self command to change the default BGP next-hop settings.
After this command is configured, R2 advertises a next hop of 192.168.2.2 (the IP address of its loopback interface) to its IBGP neighbor because that is the source IP address of the routing update to its IBGP neighbor (set with the neighbor update-source command).

## Slide 14: BGP Synchronization
The BGP synchronization rule states that:
  “A BGP router should not use, or advertise to an external neighbor, a route learned by IBGP, unless that route is local or is learned from the IGP.”
  If synchronization is enabled, a router learning a route via IBGP waits until the IGP has propagated the route within the autonomous system and then advertises it to external peers.
  With the default of synchronization disabled, BGP can use and advertise to external BGP neighbors routes learned from an IBGP neighbor that are not present in the local routing table.
BGP synchronization is disabled by default in Cisco IOS Software Release 12.2(8)T and later.
  It was on by default in earlier Cisco IOS Software releases.

## Slide 15: Synchronization
When an AS provides transit service to other ASs and if there are non-BGP routers in the AS, transit traffic might be dropped if the intermediate non-BGP routers have not learned routes for that traffic via an IGP
The BGP synchronization rule states that BGP should not advertise a route until all of the routers within the AS have learned about the route via an IGP
Designed for when an AS provides transit service to another AS
BGP will wait until the IGP has propagated the route within the AS and then it will advertise that route to external peers
BGP router will not advertise iBGP routes (learned from iBGP peer) unless the route also exists within the IGP table thus considered synchronised

## Slide 16: Synchronisation cont…
Router B will not advertise 170.10/16 to D until also learned from E via IGP

## Slide 17: Synchronisation cont…
Disabling synchronization allows BGP to converge more quickly, but it might result in dropped transit packets
You can disable synchronization if one of the following conditions is true:
Your AS does not pass traffic from one AS to another AS
All the transit routers in your AS run BGP
Disabled by default in recent IOS (can’t be enabled in Junos at all)
router bgp <AS>
no synchronization

## Slide 18: Troubleshooting
Are the peers up ?
IP3AK1-B21#show ip bgp summary
BGP router identifier 172.28.154.126, local AS number 64512
BGP table version is 11, main routing table version 11
6 network entries using 606 bytes of memory
6 path entries using 288 bytes of memory
2 BGP path attribute entries using 120 bytes of memory
1 BGP AS-PATH entries using 24 bytes of memory
0 BGP route-map cache entries using 0 bytes of memory
0 BGP filter-list cache entries using 0 bytes of memory
BGP using 1038 total bytes of memory
BGP activity 7/1 prefixes, 8/2 paths, scan interval 60 secs
Neighbor V AS MsgRcvd MsgSent TblVer InQ OutQ Up/Down State/PfxRcd
192.168.3.3 4 200 0 0 0 0 0 never Idle
172.18.43.111 4 4771 137922 138093 11 0 0 1w0d 8

## Slide 19: Are the peers up ?
Common reasons why not:
Wrong AS - will see event log messages
Wrong neighbour IP
Missing eBGP multihop command for non directly connected eBGP peer
Missing update source loopback command when wanting to source from loopback
No route to neighbour – is it learned via IGP
ACL / Firewall blocking BGP – TCP 179

## Slide 20: Route is in BGP table but not Route table
If route is not valid or reachable – Route is stored in local BGP table but not advertised and not put in local Route table
Common reasons why not Valid:
No route to next-hop – require next-hop self ? or redistribution ?
Synchronisation is enabled and route does not exist in route table

## Slide 21: RIB Failure
R1> show ip bgp
BGP table version is 5, local router ID is 200.200.200.1
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal, r RIB-failure
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
r> 6.6.6.0/24 10.10.13.3 0 130 0 30 i
*> 7.7.7.0/24 10.10.13.3 0 125 0 30 i
Most common reason = Route with better administrative distance present in IGP e.g static route = don’t worry
BGP routes not used due to higher admin distance are still advertised to all BGP peers (Can override with bgp suppress-inactive)

## Slide 22: Verifying BGP: show ip bgp rib-failure
Displays BGP routes that were not installed in the RIB and the reason that they were not installed.
In this example, the displayed routes were not installed because a route or routes with a better administrative distance already existed in the RIB.
R1# show ip bgp rib-failure
Network Next Hop RIB-failure RIB-NH Matches
172.31.1.0/24 172.31.1.3 Higher admin distance n/a
172.31.11.0/24 172.31.11.4 Higher admin distance n/a
Notes: The O code indicates that the route was learned from OSPF; the IA code indicates that the learned route is in another area (interarea). The 10.2.1.0 subnet is learned on FastEthernet 0/0 via neighbor 10.64.0.2. The [110/782] in the routing table represents the administrative distance assigned to OSPF (110) and the total cost of the route to subnet 10.2.1.0 (cost of 782).

## Slide 23: How to originate a route
4 ways to originate a route
network command = any route in IGP route table
aggregate = at least 1 subnet of aggregate in BGP table
redistribute
inject-map

## Slide 24: Originating a route – Network command
The command does not start BGP on specific interfaces
Will inject into BGP any prefix that has an exact match in the route table
  If the mask is absent, only the classful network is advertised
Origin attribute = i
router bgp 100
network 200.22.0.0 mask 255.255.0.0

## Slide 25: BGP Route Must Be in IP Routing Table
It is important to understand that any network (both address and mask) must exist in the routing table for the network to be advertised in BGP.
For example, to summarize many networks and advertise a CIDR block 192.168.0.0/16, configure:
    network 192.168.0.0 mask 255.255.0.0
    ip route 192.168.0.0 255.255.0.0 null0
Now BGP can find an exact match in the routing table and announce the 192.168.0.0/16 network to its neighbors.
  The advertised static route would never actually be used since BGP would contain longer prefix matching routes in its routing table.

## Slide 26: Originating a Route - Redistribution
Redistribution
router bgp 100
redistribute connected ..
redistribute static ..
redistribute rip ..
redistribute eigrp <AS> ..
redsitribute ospf <Process id> ..
redistribute isis ..

## Slide 27: Redistribution cont …
Origin attribute = ?
Can use a route-map to set attributes etc during redistribution
e.g to redistribute all external OSPF routes into BGP and set the local preference attribute to be 50
router bgp 100
redistribute ospf 1 match external route-map SET-LOCAL-PREF
route-map SET-LOCAL-PREF permit 10
set local-preference 50

## Slide 28: Redistribution Cont…
By default only eBGP learned routes can be redistributed from BGP into an IGP
To permit redistribution of iBGP routes use:
router bgp 100
bgp redistribution-internal

## Slide 29: Default Route
By default, the redistribute command does not permit a default route to be redistributed into BGP
To permit the redistribution of the default route configure:
router bgp <AS>
default-information originate
The default can also be configured per neighbour
In this case the route does not need to be present in the route table before the default is advertised
Outbound route-maps are not applied to this default
router bgp <AS>
neighbour <ip> default-information originate

## Slide 30: Route Maps
Route maps can be used with the redistribute command
  Route maps can also be implemented using the neighbor <ip> route-map command
Route maps can be used with BGP to assign or alter BGP attributes as well as filter routes

## Slide 31: Implementing Route Maps in BGP
neighbor {ip-address | peer-group-name} route-map map-name {in | out}
Router(config-router)#
Applies the route-map to filter incoming or outgoing BGP routes to a neighbor.
route-map map-tag [permit | deny] [sequence-number]
Router(config)#
Defines the route map conditions.
match {criteria}
Router(config-route-map)#
Defines the criteria to match.
set {actions}
Router(config-route-map)#
Defines the action to be taken on a match.

## Slide 32: match Commands Used in BGP
Command | Description
match as-path | Matches the AS_PATH attribute
match ip address | Matches any routes that have a destination network number address that is permitted by a standard or extended ACL
match metric | Matches routes with the metric specified
match community | Matches a BGP community
match interface | Matches any routes that have the next hop out of one of the interfaces specified
match ip next-hop | Matches any routes that have a next-hop router address that is passed by one of the ACLs specified
match ip route-source | Matches routes that have been advertised by routers and access servers at the address that is specified by the ACLs
match route-type | Matches routes of the specified type
match tag | Matches tag of a route
* Partial list

## Slide 33: match ip-address Command
Specify criteria to be matched using ACLs or prefix lists.
Router(config-route-map)#
match ip address {access-list-number | name} [...access-list-number | name] | prefix-list prefix-list-name [..prefix-list-name]
Parameter | Description
access-list-number ¦ name | The number or name of a standard or extended access list to be used to test incoming packets. If multiple access lists are specified, matching any one results in a match.
prefix-list prefix-list-name | Specifies the name of a prefix list to be used to test packets. If multiple prefix lists are specified, matching any one results in a match.

## Slide 34: set Commands Used in BGP
Command | Description
set weight | Sets the BGP weight value
set local-preference | Sets the LOCAL-PREF attribute value
set as-path | Modifes an AS path for BGP routes
set origin | Sets the ORIGIN attribute value
set metric | Sets the Multi-Exit_Disc (MED) value
set community | Sets the BGP communities attribute
set automatic-tag | Computes automatically the tag value
set ip next-hop | Indicates which IP address to output packets
set interface | Indicates which interface to output packets
set ip default next-hop | Indicates which default IP address to use to output packets
set default interface | Indicates which default interface to use to output packets
* Partial list

## Slide 35: Weight
Highest preferred
Cisco proprietary
local significance only – not advertised to any peer
Used to influence outbound path preference
Configured on ingress
Locally originated routes have weight of 32768

## Slide 36: set weight Command
Specify the BGP weight for the routing table.
Router(config-route-map)#
set weight number
The number is the weight value.
  It can be an integer ranging from 0 to 65535.
The implemented weight is based on the first matched AS path.
Weights assigned with this command override the weights assigned using the neighbor weight command.

## Slide 37: Local Preference
Highest preferred
Used to influence outbound path preference
Configured on ingress
Not advertised outside of local AS
Default = 100

## Slide 38: set local-preference Command
Specify a preference value for the AS path.
Router(config-route-map)#
set local-preference number-value
The number-value is the preference value.
  An integer from 0 to 4294967295.
  Default 100.

## Slide 39: AS Path
Autonomous System (AS) is a connected group of IP networks that adhere to a single and clearly defined routing policy
Local AS is prepended to routes advertised to eBGP peers
Shortest AS path preferred
Used for loop prevention
Prefix not accepted if its AS_PATH contains local AS

## Slide 40: set as-path Command
Modify an AS path for BGP routes.
Router(config-route-map)#
set as-path {tag | prepend as-path-string}
Parameter | Description
tag | Converts the tag of a route into an autonomous system path. Applies only when redistributing routes into BGP.
prepend | Appends the string following the keyword prepend to the AS path of the route that is matched by the route map. Applies to inbound and outbound BGP route maps.
as-path-string | AS number to prepend to the AS_PATH attribute. The range of values for this argument is 1 to 65535. Up to 10 AS numbers can be entered.
Notes: In Cisco IOS Release 12.0(32)SY8, 12.0(33)S3, 12.2(33)SRE, 12.2(33)XNE, 12.2(33)SXI1, Cisco IOS XE Release 2.4, and later releases, 4-byte autonomous system numbers are supported in the range from 65536 to 4294967295 in asplain notation and in the range from 1.0 to 65535.65535 in asdot notation.
In Cisco IOS Release 12.0(32)S12, 12.4(24)T, and Cisco IOS XE Release 2.3, 4-byte autonomous system numbers are supported in the range from 1.0 to 65535.65535 in asdot notation only.
For more details about autonomous system number formats, see the router bgp command.

## Slide 41: AS Path cont …
192.0.2.0/24
Notes: 192.0.2.0/24 behind AS1

## Slide 42: AS Path Prepending
AS path prepending used to influence inbound path selection
Add 1 or more occurrences of local AS to AS path causing it to be less favourable
Configure on egress
router bgp 100
neighbor 10.1.1.12 remote-as 200
neighbor 10.1.1.12 route-map prepend out
route-map prepend permit 10
set as-path prepend 100 100

## Slide 43: Origin
Indicates how a route was learned by BGP
Order of preference - IGP, EGP, Incomplete
Origin Codes:
i Entry originated from Interior Gateway Protocol (IGP) and was advertised with a network router configuration command
e Entry originated from Exterior Gateway Protocol (EGP) not to be confused with eBGP
? Origin of the path is not clear. Usually, this is a router that is redistributed into BGP from an IGP

## Slide 44: MED – Multi Exit Discriminator (aka Metric)
Lowest preferred
Used to influence inbound path selection. Configure on egress
MED received from a neighboring AS will not be propagated to other neighboring ASes. Is propagated within local AS
Default MED = 0 (or IGP metric when redistributed into BGP)
Only compared if the first AS in a routes AS sequence (neighbouring AS) is the same
Paths with no MED are set to MED 0 (Cisco)
Can enable bgp bestpath med missing-as-worst, then paths with no MED are assigned a MED of 4,294,967,294

## Slide 45: set metric Command
Specify a preference value for the AS path.
Router(config-route-map)#
set metric metric-value
The metric-value is use to set the MED attribute.
  An integer from 0 to 294967295.